## Slide 1
Forecasting the intermittent solar resource
Cyril Voyant, Research Director — Mines Paris – PSL, Centre O.I.E., Sophia Antipolis
UE14 — Mines Paris engineering curriculum (English version of the 2026 course)
Applied research project: modelling and forecasting global solar irradiance
MINES PARIS – PSL
CENTRE O.I.E.
SOPHIA ANTIPOLIS
Cite as: Voyant, C. (2026). Forecasting the intermittent solar resource (UE14 course, English version). Mines Paris – PSL. Licence CC BY 4.0.
Web companion with the worked example: cyrilvoyant.github.io/teaching/solar-forecasting-basics.html

## Slide 2
Course outline
2
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
01
Why forecast solar power?
Grid issues, units, the Ajaccio data
02
Solar radiation
Direct, diffuse, atmosphere, Sun position
03
Time series and forecasting
Components, horizon, a first AR(1) model
04
Clear sky and clear-sky index
Solis model, CSI, stationarity
05
AR model and least squares
Building X and y, least squares, choosing p
06
Evaluation, ELM and online learning
Persistence, metrics, ELM, sliding window, frugality
Appendices: wide-sense stationarity, conditional expectation, AIC/BIC criteria. Glossary and references at the end.

## Slide 3
Project objectives
3
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Context
Solar irradiance is intermittent (clouds).
The power grid must anticipate photovoltaic production.
Need: reliable short-term forecasts (here 1 h).
By the end, you will be able to
compute a clear-sky index (CSI);
build and estimate an AR(p) model by least squares;
build an ELM and measure its variability;
compare models with persistence (MAE, RMSE, skill score);
update a model online and judge its frugality.
The full chain we will build
1
GHI
measurements
2
Clear sky
GHIcs
3
CSI index
(difference)
4
Centring
y = CSI − μ
5
Chronological
split
6
Model
P · AR · ELM
7
Forecast
ŷt+h
8
Forecast GHI
ŷ + μ + GHIcs
9
Evaluation
day · day+night
This chain comes back in every chapter; the current step is highlighted.

## Slide 4
Notation (used throughout the course)
4
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Symbol | Meaning
GHIt | global horizontal irradiance measured at hour t (Wh/m²)
GHIcst | clear-sky GHI (Solis model)
CSIt | clear-sky index: GHIt − GHIcst (Wh/m²)
yt | centred CSI, the modelled series: yt = CSIt − μ
ŷt+h | forecast of y made at t for t + h
h | horizon, in number of steps (1 step = 1 h)
p | number of lags (past values used)
GHIfct+h | ŷt+h + μ + GHIcst+h; 0 at night or if negative
et | forecast error: GHIfct − GHIt
μ | mean CSI (training period)
Symbol | Meaning
X, y | input matrix, target vector
w | AR model coefficients
εt | error (unpredictable part)
Win, b | random ELM weights and biases
H, β, L | hidden outputs, output weights, number of neurons
θz, δ, ω, φ | zenith angle, declination, hour angle, latitude
α; W | ridge regularization; sliding-window length
N | number of examples (rows of X)
Δt | time step (here 1 h)
Convention: bold lower case = vector, bold upper case = matrix, plain = number. Time is always a subscript: yt, yt−1, CSIt+h.

## Slide 5
1 · Why forecast solar power?
Why forecast? Grid and solar production
5
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
The grid operator balances PV, storage, other plants and consumers.
Solar output varies with clouds. To integrate it into the grid, it must be anticipated.
Grid stability
Anticipate production drops to keep the frequency stable.
Storage
Charge or discharge batteries at the right time.
Supply / demand balance
Adjust the other plants (hydro, pumped storage*, gas…).
Economic value
Sell production at the best price and cut operating costs.
* Pumped-storage hydropower: a reversible dam that stores energy by pumping water uphill.

## Slide 6
1 · Why forecast solar power?
Irradiance, irradiation and photovoltaic output
6
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Irradiance (W/m²)
Power received per m² at a given instant. Example: 1,000 W/m² in full sun at noon.
Irradiation (Wh/m²)
Energy received per m² over a duration. Over one hour: hourly irradiation in Wh/m² = mean irradiance in W/m².
Our data
Hourly GHI in Wh/m². Météo-France files are in J/cm²: 1 J/cm² = 2.78 Wh/m², so Wh/m² = J/cm² / 0.36.
From irradiance to electrical power
P ≈ η · S · G
η: module efficiency (≈ 20 %), S: area (m²), G: irradiance on the module (W/m²).
Example: 10 m² under 800 W/m² → P ≈ 0.20 × 10 × 800 = 1.6 kW.
Output is proportional to irradiance: forecasting GHI is forecasting production.

## Slide 7
1 · Why forecast solar power?
The dataset: Ajaccio, 1998–2007
7
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Hourly GHI measured at Ajaccio in 2007 (Météo-France).
Site: Ajaccio (Corsica), 41.9° N, 8.8° E, 4 m.
Variable: hourly GHI (Wh/m²).
Period: 1998–2007, i.e. 87,600 hours.
Maximum: 1,025 Wh/m².
Daytime mean: 368 Wh/m².
Ten years of measurements: 8 years to learn, 1 year to tune the model, 1 year to test it (chapter 5).

## Slide 8
2 · Solar radiation
Components of global radiation
8
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Direct (DNI)
Received straight from the Sun, measured on a surface perpendicular to the rays (direct normal). Dominant under clear sky.
Diffuse (DHI)
Scattered by air, aerosols and clouds. Dominant under overcast sky.
Reflected (albedo)
Sent back by the ground. Counts only for a tilted surface, not for GHI.
θz: zenith angle (between the Sun and the vertical). GHI = Global Horizontal Irradiance.

## Slide 9
2 · Solar radiation
Crossing the atmosphere
9
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Through the atmosphere, radiation is attenuated by four mechanisms.
Absorption
Water vapour, ozone, CO₂: part of the energy is absorbed.
Rayleigh scattering
By air molecules: it makes the sky blue.
Mie scattering
By aerosols (dust, sea salt, pollution): depends on turbidity.
Clouds
Reflection, scattering and absorption: main cause of intermittency.
Ajaccio, 2007: a clear day and an overcast day.
Under overcast sky, GHI drops here to about 20 % of its clear-sky value.

## Slide 10
2 · Solar radiation
The position of the Sun
10
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Solar elevation over the day at Ajaccio, by season.
Zenith angle θz: between the Sun and the vertical. The larger it is, the thicker the atmosphere crossed.
Declination δ: angle between the Sun's direction and the equatorial plane; from −23.45° to +23.45° over the year.
Hour angle ω: 15° per hour, zero at solar noon. Latitude φ: 41.9° at Ajaccio.
cos θz = sin φ · sin δ + cos φ · cos δ · cos ω
G0 = I0 · (d0/d)2 · cos θz
G0: extraterrestrial radiation; I0 ≈ 1361 W/m² (solar constant; 1367 in older codes).
The Earth–Sun distance d varies by ±1.7 %, so (d0/d)2 varies by ±3.3 %.

## Slide 11
2 · Solar radiation
The double seasonality of GHI
11
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Hourly GHI in 2007: hours of the day × days of the year (Ajaccio).
Daily seasonality
Zero at night, maximum around solar noon: a 24-h cycle well described by the clear-sky model.
Annual seasonality
The amplitude of the daily cycle changes with the season (declination, day length): a 365-day cycle.
Raw GHI is not stationary: its mean depends on the hour and the month. Both cycles must be removed before modelling.

## Slide 12
3 · Time series and forecasting
What is a time series?
12
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
A sequence of measurements y1, y2, …, yN of one quantity, taken at a constant time step Δt. Here Δt = 1 h.
Three properties
Regularity: measurements are equally spaced.
Dependence: the past informs the future.
Randomness: each value has an unpredictable part.
What we want for modelling
Stationarity: stable mean and variance over time.
Complete series: no missing values.
Ajaccio: one week of hourly GHI.
Raw GHI is not stationary (day/night and seasonal cycles): that is the whole point of chapter 4.

## Slide 13
3 · Time series and forecasting
Components of a time series
13
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Trend Tt
Slow long-term change: increasing, decreasing or none.
Seasonality St
Regular, repeatable cycles (day, year). Very strong for GHI.
Cycle Ct
Long, not strictly periodic oscillations (climate phenomena).
Residual Rt
Unexplained random part. Ideally white noise (independent values, zero mean).
For GHI: seasonality dominates, with two cycles (daily and annual).

## Slide 14
3 · Time series and forecasting
Decomposing a time series
14
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Additive model
yt = Tt + St + Ct + Rt
When the amplitude of fluctuations stays constant.
Multiplicative model
yt = Tt × St × Ct × Rt
When the amplitude grows with the level (GHI: small in winter, large in summer).
Why decompose?
Remove trend and seasonality (the part predictable without effort);
keep a residual that is easier to model;
check that this residual looks like white noise.
Link with what follows: subtracting clear-sky GHI, CSIt = GHIt − GHIcst, applies the additive model: both cycles go at once. The ratio (multiplicative model) also exists: chapter 4.

## Slide 15
3 · Time series and forecasting
Horizon, time step and types of forecast
15
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Usual methods by horizon (orders of magnitude).
Time step Δt = 1 h; horizon h in steps: h = 1 → 1 h, h = 3 → 3 h.
Direct forecast: one model trained for each horizon h.
Recursive forecast: forecast t + 1, then feed that forecast back to forecast t + 2, and so on.
In this course: 1-h horizon, direct forecast.

## Slide 16
3 · Time series and forecasting
Forecasting: a predictable part and an error
16
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
yt+1 = f(yt, yt−1, …, yt−p+1) + εt+1
The predictable part
f sums up what the past tells us about the future. The forecast is ŷt+1 = f(yt, …, yt−p+1).
The error
εt+1 = yt+1 − ŷt+1 is the unpredictable part. If the model is good, ε looks like white noise.
The goal
Choose f so that errors are as small as possible in mean square.
The framework suits GHI: regular measurements and strong hour-to-hour dependence (cloud inertia). Further reading: appendix B.

## Slide 17
3 · Time series and forecasting
A first example: the AR(1) model, with numbers
17
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
yt+1 = w · yt + εt+1
yt = CSIt − μ: gap of the CSI to its mean; w: weight of the last gap.
|w| < 1: the series always returns to its mean.
ŷt+h = wh · yt
Ajaccio: μ ≈ −33 Wh/m² and w ≈ 0.84. A cloud: CSIt = −300 Wh/m², so yt = −267.
ŷt+1 = 0.84 × (−267) = −224: forecast CSI = −257 Wh/m²; then −221 and −191 at 2 h and 3 h.
The forecast CSI returns to its mean as h grows.

## Slide 18
4 · Clear sky and clear-sky index
The clear-sky model
18
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
What is it?
The GHI one would measure without clouds, given the Sun's position and a clear atmosphere.
Inputs
site position (latitude, longitude, altitude);
Sun position (θz);
water vapour and aerosols (AOD: aerosol optical depth).
Role: GHIcst is the reference used to remove the day/night and seasonal cycles.
Beer–Lambert law: intensity decays exponentially with the path length crossed.

## Slide 19
4 · Clear sky and clear-sky index
The Solis model
19
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Solis (Ineichen, 2008) is a simplified version of a radiative-transfer model. It starts from the Beer–Lambert law:
GHIcs ≈ I0 · exp(−τ / cos θz) · cos θz
τ: optical depth (air, water vapour, aerosols);
Solis adjusts τ and the exponent for water vapour, aerosols and altitude.
Settings: rural zone, water column 3.79 cm, AOD 0.16, I0 = 1367 W/m².
The hourly value is the mean of the past hour: the Sun is computed at mid-hour, ω = (i − 12.5) × 15°.
Mean clear-sky error at Ajaccio: ≈ 32 Wh/m².
Ajaccio, 2007: Solis and measurement under clear sky.

## Slide 20
4 · Clear sky and clear-sky index
Stationarizing: the clear-sky index (CSI)
20
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
CSIt = GHIt − GHIcst
≈ 0 under clear sky, and 0 at night;
negative under clouds (down to −GHIcs);
mean μ ≈ −33 Wh/m²: we centre it, yt = CSIt − μ.
The procedure
1. compute GHIcs, then the CSI;
2. centre: yt = CSIt − μ;
3. forecast ŷt+h;
4. rebuild GHIfct+h = ŷt+h + μ + GHIcst+h (0 at night, never negative).
Ajaccio, 2007: top, GHI; bottom, CSI. The daily cycle has gone from the CSI.

## Slide 21
4 · Clear sky and clear-sky index
Two ways to stationarize
21
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
The Solis model removes the cycles in two ways:
Difference (additive model) — this course
CSIt = GHIt − GHIcst, in Wh/m²;
no division: valid day and night (at night, 0 − 0 = 0);
all hours are kept, no filtering.
Ratio (multiplicative model)
kt = GHIt / GHIcst, unitless (≈ 1 under clear sky); widely used in the literature;
at night: 0 / 0, undefined; at sunrise and sunset, GHIcs ≈ 0: values explode;
requires filtering on solar elevation (for instance keep h > 10°).
For hourly data with nights, the ratio is poorly suited: we use the difference. The ratio is also very sensitive to small timestamp offsets and to the filtering thresholds chosen (Voyant et al., 2025a; 2026).

## Slide 22
4 · Clear sky and clear-sky index
Is the CSI stationary?
22
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Mean ± standard deviation by month, daytime hours, Ajaccio 1998–2007.
GHI: the mean ranges from 163 to 521 Wh/m² depending on the month.
CSI: the mean stays between −105 and −43 Wh/m², close to 0.
The CSI standard deviation still varies (97 to 185 Wh/m²): more clouds in spring.
The CSI is approximately stationary: much more than GHI, though not perfectly. Formal definition: appendix A.

## Slide 23
4 · Clear sky and clear-sky index
Site variability: the sCV
23
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
How far does GHI depart, on average, from clear sky? We measure the gap εt = GHIt − GHIcst (the CSI):
sCV = (√2 / (1 − d)) · √[ Σt (GHIt − GHIcst)2 / Σt (GHIcst)2 ]
Numerator: typical size of the gaps to clear sky (the clouds).
Denominator: typical size of clear-sky GHI.
√2 / (1 − d) scales the worst case to 1: clear sky, then very overcast, every other hour (d = 0.2: even under overcast sky, at least 20 % of clear sky remains).
sCV = 0: always clear; sCV = 1: maximum variability. It does not depend on the horizon: it is a property of the site.
Ajaccio 1998–2007: sCV and F at 1 h, month by month (Voyant et al., 2026).
Ajaccio: sCV = 0.52 over 1998–2007.
Winter: 0.8 (changeable sky); July: 0.3 (often clear sky).

## Slide 24
4 · Clear sky and clear-sky index
Forecastability: F depends on the horizon
24
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
A variable series is not necessarily unpredictable: if the gaps to clear sky last, they can be anticipated.
ρ(k): correlation between the clear-sky gap now, εt, and k hours later, εt+k (the memory of clouds).
ρmax(h): the strongest of these correlations for k between h and 12 h: the memory left when forecasting at horizon h.
F(h) = 1 − sCV · (1 − ρmax(h))
perfect memory (ρmax = 1): F = 1, everything is predictable;
no memory (ρmax = 0): F = 1 − sCV.
Ajaccio 1998–2007: F and remaining memory by horizon (Voyant et al., 2026).
F = 0.92 at 1 h, 0.74 at 3 h, 0.53 at 6 h.
The atmosphere is chaotic: cloud memory fades within a few hours. sCV does not move.

## Slide 25
4 · Clear sky and clear-sky index
Pre-processing step by step
25
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
1
GHI
measurements
2
Clear sky
GHIcs
3
CSI index
(difference)
4
Centring
y = CSI − μ
5
Chronological
split
6
Model
P · AR · ELM
7
Forecast
ŷt+h
8
Forecast GHI
ŷ + μ + GHIcs
9
Evaluation
day · day+night
1 · Measurements
Hourly GHI, converted from J/cm² to Wh/m² (÷ 0.36).
2 · Clear sky
GHIcs by Solis, Sun at mid-hour, over a typical year.
3 · CSI
CSIt = GHIt − GHIcst, every hour.
4 · Centring
yt = CSIt − μ with μ ≈ −33 Wh/m²: series ready for AR and ELM.
With the difference, nights cause no problem (0 − 0 = 0): no filtering on solar elevation, unlike the ratio.

## Slide 26
5 · AR model and least squares
From the AR model to linear regression
26
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
An AR(p) model forecasts the next value from the last p values:
yt+1 = w1 yt + w2 yt−1 + … + wp yt−p+1 + εt+1
Matrix form
y = X w + ε
y (N × 1): the values to forecast;
X (N × p): one row per example, with the p lags;
w (p × 1): the coefficients to estimate;
ε (N × 1): the errors.
It is a multiple linear regression. Since y is centred, no intercept is needed.

## Slide 27
5 · AR model and least squares
Building X and y: a worked example
27
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Five centred CSI values (Wh/m²): y1 = −10; y2 = −25; y3 = −240; y4 = −180; y5 = −30. Take p = 2.
Row | yt | yt−1 | Target yt+1
t = 2 | −25 | −10 | −240
t = 3 | −240 | −25 | −180
t = 4 | −180 | −240 | −30
The two middle columns form X (3 × 2), the last one forms y (3 × 1).
Each row shifts the previous one by one step.
In practice: all hours are kept, nights included (at night, y = −μ ≈ 33). At Ajaccio: 8 years, about 70,000 rows for training.

## Slide 28
5 · AR model and least squares
Ordinary least squares (OLS)
28
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
We look for the w that minimizes the sum of squared errors:
J(w) = ‖y − Xw‖2 = Σi (yi − xiT w)2
At the minimum, the derivative is zero:
−2 XT(y − Xw) = 0 ⟹ XTX w = XTy
Conditions: many more examples than coefficients (N ≫ p);
columns of X not proportional to each other.
ŵ = (XTX)−1 XTy
Exact solution, in one step: no iteration, a single minimum.
Ajaccio, AR(2): ŵ = (0.97; −0.15), computed in 5 ms.
The last gap yt weighs by far the most.

## Slide 29
5 · AR model and least squares
Geometric interpretation
29
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Xŵ is the point of the “plane of the columns of X” closest to y: its orthogonal projection.
The error ε = y − Xŵ is perpendicular to this plane.
Pythagoras: ‖y‖2 = ‖ŷ‖2 + ‖ε‖2. This is the basis of the R2 coefficient.
OLS does not “guess” anything: it projects the measurements onto what the inputs can explain.

## Slide 30
5 · AR model and least squares
Training, validation, test
30
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Training
1998 – 2005
Validation
2006
Test
2007
time
Training
Coefficients are estimated (w, β).
Validation
Hyperparameters (p, L) are chosen without touching the test.
Test
Performance is measured once, on data never seen.
Chronological split, never shuffled: the past is not forecast with the future. After validation, re-estimate on training + validation.

## Slide 31
5 · AR model and least squares
Choosing p (1/3): autocorrelation (ACF)
31
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
ACF of the centred CSI, Ajaccio 1998–2005, all hours.
ACF(k): correlation between yt and yt−k, the value k hours earlier.
Here ACF(1) = 0.84, ACF(2) = 0.67, ACF(3) = 0.50: it decays slowly.
But this correlation propagates step by step: if yt depends on yt−1, which depends on yt−2, then yt and yt−2 are correlated even without a direct link.
The ACF therefore does not tell how many lags are really useful. The PACF is needed.

## Slide 32
5 · AR model and least squares
Choosing p (2/3): partial autocorrelation (PACF)
32
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
PACF of the centred CSI, Ajaccio 1998–2005, all hours.
PACF(k): once yt−1, …, yt−k+1 are known, what does yt−k add? It is the last coefficient wk of an AR(k).
A bar outside the blue band: this lag brings direct information.
For a true AR(p), the PACF vanishes after lag p.
Here PACF(1) = 0.84, PACF(2) = −0.15, then values below 0.08: the PACF suggests p ≈ 2.
But with N ≈ 70,000 points, the ±0.007 threshold is tiny: almost everything is “significant”. Significant ≠ useful.

## Slide 33
5 · AR model and least squares
Choosing p (3/3): filter or wrapper approach
33
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Filter
look at the data alone, before any model: PACF, AIC / BIC criteria (appendix C);
fast, but indirect.
Wrapper
train an AR(p) for p = 1 to 12 on 1998–2005;
measure the forecast error on validation (2006);
driven by the real objective, but more costly.
Wrapper approach: validation RMSE (2006, daytime hours) versus p.
p = 1: 78.0; p = 2: 77.7; p = 12: 77.3 Wh/m². Parsimony: the smallest p within 0.5 % of the best, i.e. p = 2.

## Slide 34
5 · AR model and least squares
Summary: forecasting GHI with an AR(p)
34
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
1
GHI
measurements
2
Clear sky
GHIcs
3
CSI index
(difference)
4
Centring
y = CSI − μ
5
Chronological
split
6
Model
P · AR · ELM
7
Forecast
ŷt+h
8
Forecast GHI
ŷ + μ + GHIcs
9
Evaluation
day · day+night
1. Compute GHIcs (Solis), then CSIt = GHIt − GHIcst; centre it: yt = CSIt − μ.
2. Split: training / validation / test.
3. Choose p on validation.
4. Build X and y; estimate ŵ = (XTX)−1XTy.
5. Forecast ŷt+1 = ŵT xt with xt = (yt, …, yt−p+1).
6. Rebuild GHIfct+1 = ŷt+1 + μ + GHIcst+1; set 0 at night (Sun below the horizon) and 0 if the forecast is negative.
7. Evaluate on 2007: daytime, then day + night.
Simple, fast, interpretable: it is the linear reference to beat.

## Slide 35
6 · Evaluation, ELM and online learning
Reference models
35
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Every model must be compared with a simple reference. If it does not do better, it adds nothing.
Simple persistence
“It will be as it is now.”
GHIfct+1 = GHIt
Ignores the Sun's course.
Clear sky
“It will be sunny.”
GHIfct+1 = GHIcst+1
Ignores clouds.
Smart persistence
“The sky will stay the same.”
GHIfct+1 = GHIt − GHIcst + GHIcst+1
Keeps the same gap to clear sky.
Smart persistence = AR(1) with w = 1: the reference of the skill score SS.
Two rules, for every model: 1) at night (Sun below the horizon, θz > 90°), forecast = 0; 2) a negative forecast is replaced by 0.

## Slide 36
6 · Evaluation, ELM and online learning
Measuring the error
36
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
et = GHIfct − GHIt (forecast error)
nMBE = [(1/N) Σ et] / mean(GHIt)
MAE = (1/N) Σ |et|
RMSE = √[(1/N) Σ et2] ; nRMSE = RMSE / mean(GHIt)
nMBE (bias): > 0 if the model over-estimates on average, < 0 if it under-estimates. Errors of opposite sign cancel: it is not a score for ranking models.
MAE: mean error, in Wh/m², easy to interpret.
RMSE: penalizes large errors more (sudden cloud). Always ≥ MAE.
nRMSE: RMSE as % of mean GHI, to compare sites.
Essential check: if |nMBE| > 1 %, there is probably a problem, or a very poor model. The bias can be removed, provided this is tested; we do not do it here.
Errors are computed on the rebuilt GHI, over the test year (2007): first on daytime hours, then day + night. Always say which!

## Slide 37
6 · Evaluation, ELM and online learning
Comparing with persistence: SS and NICEΣ
37
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
SS = 1 − RMSEmodel / RMSEsmart persistence
Skill score: > 0 if smart persistence is beaten, < 0 otherwise.
Looks only at the RMSE.
NICEk = Lk(model) / Lk(simple persistence)
Lk = ((1/N) Σ |et|k)1/k ; NICEΣ = (NICE1 + NICE2 + NICE3) / 3
et = GHIfct − GHIt: the forecast error (previous slide).
k = 1: average errors (MAE); k = 2: RMSE; k = 3: large errors;
NICEΣ < 1: the model beats simple persistence on all three norms at once.
Two different references: SS compares with smart persistence, NICEΣ with simple persistence (Voyant et al., 2025b).

## Slide 38
6 · Evaluation, ELM and online learning
Results at Ajaccio: 1-hour forecast
38
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Model | RMSE day | nRMSE day | nRMSE day + night | nMBE day | SS | NICEΣ
Simple persistence | 135 | 36.4 % | 51.5 % | −0.9 % | −0.66 | 1.00
Clear sky | 148 | 39.9 % | 56.4 % | +16.4 % | −0.82 | 1.06
Smart persistence | 82 | 22.0 % | 31.0 % | +1.3 % | 0.00 | 0.59
AR(2) | 79 | 21.3 % | 30.1 % | +2.0 % | +0.03 | 0.58
ELM (L = 50, best draw) | 76 | 20.5 % | 28.9 % | +1.1 % | +0.07 | 0.55
Test 2007. Daytime: 4380 hours, mean GHI 372 Wh/m². Day + night: 8759 hours, mean GHI 186 Wh/m². RMSE in Wh/m²; SS and NICE computed on daytime hours.
Smart persistence divides the RMSE of simple persistence by 1.7. AR gains 3 % over it, ELM 7 %.

## Slide 39
6 · Evaluation, ELM and online learning
Daytime only, or day + night?
39
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
79 → 56
AR RMSE (Wh/m²)
372 → 186
Mean GHI (Wh/m²)
21 → 30 %
AR nRMSE
At night (Sun below the horizon), every model forecasts 0 by construction and is right: adding these hours lowers the RMSE (≈ ÷ √2).
But the mean GHI is halved: the nRMSE increases.
The ranking of models does not change.
An error figure without the list of hours used means nothing: always state daytime or day + night.

## Slide 40
6 · Evaluation, ELM and online learning
The bias (nMBE): effect of the two rules
40
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Rule 1 (night): when the Sun is below the horizon (θz > 90°), the forecast is 0. Rule 2: a negative forecast is replaced by 0.
nMBE: mean bias, as % of mean GHI (see “Measuring the error”). Test 2007.
Model | nMBE no rules, day | nMBE no rules, day + night | nMBE with rules, day | nMBE with rules, day + night
Simple persistence | −0.88 % | 0.00 % | −0.88 % | −1.02 %
Clear sky | +16.44 % | +16.28 % | +16.44 % | +16.28 %
Smart persistence | +0.35 % | 0.00 % | +1.25 % | +1.11 %
AR(2) | +1.49 % | −0.24 % | +2.02 % | +1.87 %
ELM | +0.69 % | −0.38 % | +1.13 % | +0.99 %
How to read this table
No rules, day + night: both persistences have an nMBE of exactly zero.
Rule 2: setting negative forecasts to 0 raises the mean (smart persistence: +0.35 % → +1.25 % in daytime).
Rule 1: the nMBE of simple persistence goes from 0 to −1.02 % over day + night (next slide).
Clear sky: +16 %: it always forecasts sunshine.
An nMBE depends on how it is computed: always state daytime or day + night, with or without rules.

## Slide 41
6 · Evaluation, ELM and online learning
Why does persistence go from 0 to −1 %?
41
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
second-to-last
daytime hour
last
daytime hour
first
night hour
Measurement
150
43
0
Persistence, no rules
…
150
43
With rule 1 (night)
…
150
0
Values in Wh/m²; 43 Wh/m² = 2007 mean of the last daytime hour.
No rules: persistence copies the previous hour's measurement. Over the year, each measurement is used once as measurement and once as forecast: the two sums are equal, nMBE = 0.
With rule 1 (night): at the first night hour the Sun is below the horizon, so the forecast 43 is replaced by 0. Every day, a forecast of about 43 Wh/m² disappears.
Over the year: 365 × 43 ≈ 15,642 Wh/m², plus 1,008 Wh/m² of small values measured at night: 16,650 Wh/m² are missing.
Relative to the GHI measured over the year (1,630,161 Wh/m²): 1.02 %, hence a day + night nMBE of −1.02 %.
A single hour per day, but it weighs heavily: the day + night mean is only 186 Wh/m², because night hours count as zero.
The rule is physically right (no Sun at night), but it changes the bias.

## Slide 42
6 · Evaluation, ELM and online learning
Forecast and measurement, hour by hour
42
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Ajaccio, October 2007: 1-h forecast.
Both models follow regular days and miss sudden changes: an arriving cloud cannot be seen in the past.

## Slide 43
6 · Evaluation, ELM and online learning
Limits of the AR model
43
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
AR(p) assumes a linear relation between the CSI and its lags. Often enough at short horizons, but not always.
Difficult situations
fast clear / overcast transitions (cloud fronts);
cloud-edge effects (GHI > GHIcs);
very variable sky (cumulus);
nonlinear links between lags.
Under-fitting
A linear model cannot capture a curved relation, even with many lags.
Saturation
Beyond some p, adding lags no longer improves anything (slide “Choosing p”).
Idea: transform the inputs nonlinearly, then keep least squares. That is the ELM.

## Slide 44
6 · Evaluation, ELM and online learning
Extreme Learning Machine (ELM): the principle
44
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
One-hidden-layer ELM (Huang et al., 2006).
A neural network with a single hidden layer.
Input weights Win and biases b are drawn at random, then frozen.
Each neuron applies a nonlinear function g (tanh, sigmoid…).
Only the output weights β are learnt, by least squares.
No gradient back-propagation: training is done in a single solve.

## Slide 45
6 · Evaluation, ELM and online learning
ELM: the formulation
45
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
The p lags of each row go through the hidden layer:
H = g(X Win + b) (N × L)
 | Model | Least-squares solution | Columns used
AR | y = Xw + ε | ŵ = (XTX)−1XTy | lags of the centred CSI
ELM | y = Hβ + ε | β̂ = (HTH + αI)−1HTy | outputs of the L neurons
Same equation, only the columns change. The small term αI (ridge regression) stabilizes the solve when L is large; at Ajaccio, α = 10−3.

## Slide 46
6 · Evaluation, ELM and online learning
ELM: choosing the number of neurons L
46
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Validation RMSE (2006, daytime hours) versus L, for p = 2.
L = 5: 85.2 Wh/m² → under-fitting.
L = 50: 75.9 Wh/m².
Beyond, no further gain: 75.8 at L = 200, 75.9 at L = 500 (risk of over-fitting).
As for p: test a few values (5 to 500) on validation and keep the smallest near-optimal one. Here L = 50.

## Slide 47
6 · Evaluation, ELM and online learning
ELM: a result that depends on the draw
47
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Input weights are random: two trainings give two different models.
Candidate search: make 20 draws and keep the one with the smallest validation error (2006).
The test (2007) is used only at the end, for the selected draw.
Selected draw: test nRMSE 20.46 %.
The 20 draws: from 20.37 to 20.51 % (mean 20.45 %).
The best on validation is not necessarily the best on test: the gap is small here, but it must be checked.
Each point: one draw. Validation 2006 (horizontal), test 2007 (vertical).

## Slide 48
6 · Evaluation, ELM and online learning
Giving the model the time: sin / cos encoding
48
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Idea: add calendar variables known in advance to the lags: the hour h and the day of year j.
Problem: coded as a number, 23:00 is “far” from 00:00, although they are neighbouring hours.
Solution: place the hour on a circle, with two variables:
(sin(2π h / 24); cos(2π h / 24)) and (sin(2π j / 365); cos(2π j / 365))
4 more columns in X. The model then “knows” the hour and the season (Voyant et al., 2025a).

## Slide 49
6 · Evaluation, ELM and online learning
Stationarize or give the time? AR and ELM
49
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Daytime nRMSE, test 2007, same protocol for the 8 variants. “No clear-sky” approach: Voyant et al., 2025a.
Inputs | AR(2) nRMSE | AR NICEΣ | ELM nRMSE | ELM NICEΣ
raw GHI | 27.6 % | 0.76 | 24.3 % | 0.66
GHI + sin/cos | 24.6 % | 0.68 | 19.7 % | 0.54
CSI | 21.3 % | 0.58 | 20.5 % | 0.55
CSI + sin/cos | 21.0 % | 0.57 | 19.9 % | 0.54
AR (linear): needs the CSI. On raw GHI, even with sin/cos, it does worse than smart persistence.
ELM (nonlinear): with sin/cos, it learns the Sun's cycle by itself, from raw GHI.
nRMSE and NICEΣ give the same ranking.

## Slide 50
6 · Evaluation, ELM and online learning
AR or ELM? The verdict
50
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
ELM strengths
fast training, a single solve;
captures nonlinear relations;
same method (OLS) as AR.
ELM limits
L must be chosen;
result varies with the draw;
less interpretable than AR;
over-fits if L grows large;
needs a lot of data.
At Ajaccio, 1 h ahead
AR(2): 2 coefficients; nRMSE 21.3 %.
ELM: 51 learnt + 150 random; nRMSE 20.5 %.
Skill score SS: +0.03 (AR) versus +0.07 (ELM).
About 100 times more coefficients (learnt + random) for 4 more points of skill score. Is the gain worth the complexity?

## Slide 51
6 · Evaluation, ELM and online learning
Online learning (1/2): the sliding window
51
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Forecast
Observe
Update
hour t
hour t + 1
blue: the W training hours; pink: the hour to forecast
Matrix X always keeps W rows: the last W hours.
Every hour, the newest row is added and the oldest removed, then ridge is re-estimated:
ŵ = (XTX + αI)−1XTy
Trick: no need to recompute everything. XTX ← XTX + xnewxnewT − xoldxoldT.
Same for the ELM, with H instead of X.
Update: 11 µs for AR, 38 µs for the ELM, per hour.
Useful when the system changes (drifting sensor, soiled panel, new site): the model forgets the distant past.

## Slide 52
6 · Evaluation, ELM and online learning
Online learning (2/2): which window length?
52
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Test 2007: every hour, ridge re-estimated on the last W hours, from 1 month to 2 years.
Short window: follows recent changes… but learns from little data.
Window W | AR(2) | ELM (L = 50)
1 month | 21.5 % | 25.6 %
3 months | 21.3 % | 21.9 %
6 months | 21.3 % | 21.2 %
1 year | 21.3 % | 20.9 %
2 years | 21.3 % | 20.7 %
8 years (fixed) | 21.3 % | 20.5 %
Daytime nRMSE over 2007 versus window length.
AR (2 coefficients) works even with 1 month. The ELM (51 coefficients) degrades clearly with a short window: the more parameters a model has, the more data it needs.

## Slide 53
6 · Evaluation, ELM and online learning
Frugality
53
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
A frugal model reaches good accuracy with little computation, little data and little maintenance.
Model | Learnt coefficients | Training cost | Data needed | nRMSE day (test)
Smart persistence | 0 | none | 1 hour | 22.0 %
AR(2) | 2 | 5 ms | 1 month is enough | 21.3 %
ELM (L = 50) | 51 (+ 150 random) | 68 ms per draw | several years | 20.5 %
AR, 1-month sliding window | 2 | 11 µs per hour | 720 hours | 21.5 %
Timings measured on a laptop: only the orders of magnitude matter.
The right question is not “which model is best?” but “does the gain justify the cost?” (computation, data, maintenance, monitoring).

## Slide 54
Thank you — your turn: the project
54
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Grid and units
Forecasting GHI is forecasting production.
Radiation
Direct, diffuse; Sun position; clouds.
Time series
Components, horizon, AR(1).
Clear sky and CSI
Solis; CSI = GHI − GHIcs, centred.
AR and OLS
ŵ = (XTX)−1XTy, choice of p.
Evaluation, ELM, online
Day / day + night, sliding window, frugality.
Cyril Voyant — cyril.voyant@minesparis.psl.eu — Mines Paris – PSL, Centre O.I.E.
Worked example on the web: cyrilvoyant.github.io/teaching/solar-forecasting-basics.html

## Slide 55
Glossary
55
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Acronym | Meaning
AR(p) | autoregressive model of order p
ACF / PACF | autocorrelation / partial autocorrelation
AIC / BIC | Akaike / Bayesian information criteria
AOD | aerosol optical depth
CSI | clear-sky index
DHI | diffuse horizontal irradiance
DNI | direct normal irradiance
ELM | Extreme Learning Machine
GHI | global horizontal irradiance
MAE | mean absolute error
OLS | ordinary least squares
Acronym | Meaning
NWP | numerical weather prediction
nRMSE | RMSE normalized by mean GHI
RMSE | root mean square error
MBE | mean bias error
sCV | stochastic coefficient of variation
F | forecastability
NICE | score relative to simple persistence
sin / cos | circular encoding of hour and day
SS | skill score
PHS | pumped-storage hydropower

## Slide 56
References
56
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
Huang G.-B., Zhu Q.-Y., Siew C.-K. (2006). Extreme learning machine: theory and applications. Neurocomputing, 70, 489–501. doi:10.1016/j.neucom.2005.12.126
Ineichen P. (2008). A broadband simplified version of the Solis clear sky model. Solar Energy, 82(8), 758–762. doi:10.1016/j.solener.2008.02.009
Voyant C. et al. (2017). Machine learning methods for solar radiation forecasting: a review. Renewable Energy, 105, 569–582. doi:10.1016/j.renene.2016.12.095
Voyant C. et al. (2022). Benchmarks for solar radiation time series forecasting. Renewable Energy, 191, 747–762. doi:10.1016/j.renene.2022.04.065
Voyant C. et al. (2026). Stochastic coefficient of variation: assessing the variability and forecastability of solar irradiance. Renewable Energy, 256, 123913. doi:10.1016/j.renene.2025.123913
Voyant C., Despotovic M., Notton G., Saint-Drenan Y.-M., Asloune M., Garcia-Gutierrez L. (2025a). On the importance of clearsky model in short-term solar radiation forecasting. Solar Energy, 289, 113490. doi:10.1016/j.solener.2025.113490
Voyant C. et al. (2025b). NICEk metrics: unified and multidimensional framework for evaluating deterministic solar forecasting accuracy. Sustainable Energy Technologies and Assessments, 81, 104588. doi:10.1016/j.seta.2025.104588
Hyndman R. J., Athanasopoulos G. (2021). Forecasting: Principles and Practice, 3rd ed. OTexts. otexts.com/fpp3
Box G. E. P., Jenkins G. M., Reinsel G. C., Ljung G. M. (2015). Time Series Analysis: Forecasting and Control, 5th ed. Wiley.
Data: Météo-France, Ajaccio station. All figures and schematics drawn by the author.

## Slide 57
Appendices
Appendix A — Wide-sense stationarity
57
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
A process (zt) is wide-sense stationary if:
E[zt] = μ (constant) and Cov(zt, zt+k) = γ(k) (depends only on the lag k)
In practice
the mean is constant over time;
the variance is finite and constant;
the dependence between two instants depends only on their gap.
Simple check: plot the mean and standard deviation month by month (slide “Is the CSI stationary?”). Statistical tests exist but are not needed here.

## Slide 58
Appendices
Appendix B — The best possible forecast
58
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
ŷt+h = E[yt+h | yt, yt−1, …, yt−p+1]
Among all forecasts built from the past, the one that minimizes the mean squared error is the conditional expectation: the mean of possible futures, given the past.
We then write yt+h = ŷt+h + εt+h: predictable part + error, with a zero-mean error.
An AR(p) model is a linear approximation of this expectation; the ELM, a nonlinear one.
If the model errors form white noise (non-significant error ACF), no usable information is left in the past.

## Slide 59
Appendices
Appendix C — Choosing p with AIC or BIC
59
Cyril Voyant · Mines Paris – PSL · Solar forecasting basics · CC BY 4.0
AIC ≈ N · ln(σ̂2) + 2(p+1)
BIC ≈ N · ln(σ̂2) + (p+1) · ln N
σ̂2: variance of the training errors;
keep the p that gives the smallest criterion.
The first term falls as the model fits better; the second penalizes each added coefficient.
BIC penalizes more than AIC: it picks smaller models.
Advantage: no validation period needed. Drawback: assumes Gaussian errors.